## Slide 1: ODIN II
TEAM 11
TODD TOWNSEND, ABRAM FOUTS, KARLA BARRAZA LOPEZ, WENHAO CHENG, XUENING JIA
Sponsor: Brad Smith - Intel Corporation
Advisor: Fu Li
Notes: Bram

## Slide 2: ODIN
Ocular Divergence reINtegration
Ocular Divergence
  Strabismus: Abnormal alignment of the eyes
Other Forms of condition:
  Amblyopia (Lazy Eye)
  Diplopia (Double Vision)
  Oculomotor Palsy (Unsteady Gaze)
  Oculomotor Paralysis (Fixed Gaze)
Notes: Bram

## Slide 3: Our Project
Using a virtual reality headset:
Obtain exact misalignment position of eye for ocular divergence patients
Use touch controllers to allow patient to control environment, manipulate space
In cooperation with neural networks, our project will manipulate the field of view
Using foveated rendering, force the ocular divergent eye to focus directly on the target
Foveated Rendering
Ocular Divergence
Field of view
Notes: Todd

## Slide 4: Deliverables
1. Gaze Vectors
  Application peripheral interface output hook
  Locate gaze vectors in Tobii software
2. Touch Controller
  Create custom trigger events
  Obtain the 3-dimensional position and angle vectors
3. Field of View
  Set up Left Camera and Right Camera
  Render each Camera with the correct vectors
  Manipulate frustum values
Notes: Todd

## Slide 5: Block Diagram
Notes: Bram

## Slide 6: Our Approach
With the COVID-19 interrupted our approach drastically
COVID forced us to do much more research than development because the lack of access to our VR machine
We referred to the SteamVR API Documentation website
  The less commonly used scripts had very little documentation
Our best friend was taking a script we think will be useful and isolating it on an object to study it
We were all hands on deck looking through the given SteamVR source code and Tobii software code
Notes: Karla

## Slide 7: Gaze Vector
X, Y, Z coordinates on a three dimensional plane
Successfully written and tested Output Function
  Output function takes X, Y, Z coordinates as arguments
Connects to Tobii API
  Unity command line display
  Gaze Vectors then sent to Comparator
Gaze Vector focusing on singular object
Notes: Todd

## Slide 8
Correction Vector
COVID-19 - Correction Vectors became a should:
Comparator Function
Takes X, Y, Z coordinates from Gaze Vector as argument
Three dimensional X, Y, Z comparison
Produce Correction Vector
Correction vector sent to Unity for Foveated Rendering then into field of view on HMD
Notes: Todd

## Slide 9: Target Vector
Exact focal position of the of the human eye focused on an object
Obtained from Calibration Test Application
  Initialized upon VR HMD calibration
CNN Neural network will determine precise 3D location and calculation
Determined by a neural matrix
Gaze Vector – Target Vector = Correction Vector
Notes: Todd

## Slide 10: Touch Controller
Replace default touch controller trigger events with our own
Each button has unique tracking
  D-pad has a boolean press and an XY coordinate touch tracker
  The trigger is treated as a boolean press and a float that varies between 0.0-1.0
  All other buttons are boolean presses
Goal: identify hooks into the position, rotation and button controls of the controller to ultimately edit FOV themselves with controller
Notes: Karla

## Slide 11: Touch Controller
With SteamVR 2.0, a bindings controller interface was introduced
  developers didn’t need to go through the redundant process of creating custom bindings
The developer simply creates functions and apply them to the corresponding trigger on either touch controller
Notes: Karla

## Slide 12: Touch Controller
Each object in unity has a transform that holds position and rotation information
We attached an action to the controller via the binding that would return the rotation and position of the controller
Location
Rotation
This screenshot was taken before the controller was actually awake
Notes: Karla

## Slide 13: Field of View (FOV)
In VR devices, the field of view refers to the field of view in the horizontal direction.
The size of the field of view directly affects the clarity and immersion of the field of view.
The highest and lowest rays we can see are refracted into the eye through the lens, and the angle between the two refractive lines is FOV.
Notes: Xuening/Wenhao/Bram

## Slide 14: Field of View
Making the left and right eyes display content separately; (Set up Left Camera and Right Camera)
Using correction vectors and apply them to the two frustums (FOV); （Move frustums through the correction vector）
Notes: Xuening/Wenhao/Bram

## Slide 15: IP
Our team owns the IP to all of the work we have done
Intel plans on us to sign it over
Intellectual property rights will be owned by Brad Smith and Intel with our signed statement
Including code, documentation, and research
Notes: Bram

## Slide 16: Testing
Once we found scripts or functions that produced or used values we were interested in we isolated them on a gameobject in Unity or our HMD
The goal was to find where certain values were being produced and extract them out
The simplest test scripts (hello world) were in place to show we found the correct function or implemented working code
We used our industry advisor and his kids as a guinea pig for every test (COVID solution)
Notes: Bram

## Slide 17: Results
Gaze Vectors:
  Automated script works together with the Tobii API
  x, y, z coordinates of gaze vector are locked and referenced in Unity API
  Raw gaze vector values are imported from Tobii API to Unity API
Touch Controllers:
  Our script connects the controller with the code and outputs location and rotation, but not live updating rotation and location
Field of View:
  Twelve point field of view vector is referenced from script to Unity API
  Dereferencing variables causes Unity to throw run-time errors
  Instances of variable types in script are not matching Unity API requirements
Notes: Todd/Karla/Bram/Xuening/Wenhao

## Slide 18: Contributions
Gaze Vectors
  Todd & Karla
Touch Controllers
  Bram & Karla
FOV
  Xuening, Wenhao & Bram
Notes: Todd/Karla/Bram/Xuening/Wenhao

## Slide 19: Conclusion
Ocular Divergence reINtegration
Is a possible corrective alternative for strabismus
Replaces current solutions
  Eye patches - Physical Therapy
  Prism Glasses
Allows for corrective healing over time
Allows for fine control of visual input
Appealing to children and gamers
Gaze training with consumer VR equipment
Reduces the probability of future corrective surgery
Notes: Todd